## Slide 1
ENT 609 AUT
1 PAGE MARKETING PLAN
City Wide EV Battery Swapping Network for Gig Workers and Commercial Drivers
Team "____________" | Members: ______________________________________
Built on seven face to face customer interviews recorded in the Customer Discovery Journals

## Slide 2
Team "____________" 1 Page Marketing Plan
City wide EV battery swapping network for gig workers and commercial drivers ENT609 2025AUT
Current Option / Cost
Petrol bike: Rs 210 to 395 per day of fuel at Rs 111.18 per litre [3]
CNG auto: Rs 325 to 390 per day at Rs 88 per kg, plus a 20 to 45 minute refuel queue [4]
Rental EV with unlimited swaps: Rs 7,000 to 9,000 per month, vehicle not owned
Pay per swap networks: Rs 120 to 250 a swap, about Rs 1.3 to 1.7 per km [6]
Home charging: 4 to 6 hours, not possible mid shift
Providers: Battery Smart (1,600+ stations), Sun Mobility with IndianOil, Honda e:Swap [2]
Key technology: lithium ion packs in locked smart cabinets with IoT enabled BMS
Bought from rental fleet operators, per swap apps and EV dealers
Customer Unmet Need
Job to be done: keep earning through the shift without stopping to charge
Charging downtime directly cuts earning hours
Nearest swap point was up to 10 km away, so trips were lost (Customer 1)
Rental at Rs 7,000 to 9,000 a month is unaffordable, so riders went back to petrol (Customer 4)
Riders want to own the vehicle and build an asset, not stay on rent (Customers 5 and 6)
Fuel price risk sits entirely on the driver
Met today: energy is available somewhere in the city
Not met: low cost, nearby, and usable on a vehicle the rider owns
Loss if unmet: 1 to 2 earning hours a day and stalled EV adoption
Customer and Market Profile
Bike taxi riders (Rapido), quick commerce delivery partners (Instamart) and CNG auto drivers
Male, age 20 to 40, monthly earning Rs 18,000 to 35,000
Daily running 80 to 150 km across 26 to 28 days a month
Habits: WhatsApp rider groups, UPI payment, platform rider hubs, regional language reels
Priorities: maximise earning hours, keep fixed monthly cost low, own the vehicle
India crossed 3,000 swap stations and USD 325 million invested by mid 2026 [1]
Market USD 33.6 million in 2026 to USD 105.5 million by 2031, CAGR 25.7 percent [1]
Addressable by Year 3: 5,400 subscribers on 120 Mumbai stations
VALUE PROPOSITION
For delivery riders, bike taxi riders and auto drivers in Mumbai who run 80 to 150 km every day
Who lose earning hours to charging and cannot afford a rental EV at Rs 7,000 to 9,000 a month
We ____________ operate a city wide battery swapping network hosted at partner petrol pumps
Offer unlimited two to three minute swaps on the rider's own electric vehicle, with no rental and no battery ownership
Which is faster than every charging option and fixed in price, unlike petrol and CNG which keep rising
At Rs 6,000 per month, unlimited swaps
Proposed Solution
20 slot smart swap cabinet hosted at partner petrol pumps, 100 to 150 sq ft
One standard module: 2.0 kWh, 48 V, LFP, 10 to 12 kg, hand liftable
Two wheeler takes 2 modules (4 kWh), electric auto takes 4 modules (8 kWh)
Interface: app with QR unlock, live station stock, UPI billing, swap history
Smart BMS with IoT tracking of cycles, temperature and state of health, AIS 156 compliant
1 kW charger per slot at 0.5C, about 2 hours per module, 20 kW load on a 25 kVA LT connection
Modules assembled and tested in house from Indian ACC cells, cabinets sourced locally
Serviced remotely, faulty packs pulled to a central depot, retrofit kit for existing fleet EVs
Better / Faster / Cheaper
Against petrol bike: Rs 0.44 per km against Rs 2.47 per km
Against CNG auto: Rs 0.44 against Rs 3.26 per km, a saving of about Rs 3,100 a month
Against rental EV: the rider owns the vehicle and saves Rs 1,000 to 3,000 a month
Against home charging: 2 to 3 minutes against 4 to 6 hours
Against CNG refuelling: 2 to 3 minutes against a 20 to 45 minute queue
Against pay per swap: one fixed monthly bill with no per trip cost anxiety
Quality: AIS 156 compliant packs, every swap logged, pack health tracked continuously
After sales: a healthy pack is handed over on the spot, the rider never waits for a repair
Unit Price / Cost
COST per station
40 packs at Rs 27,000: Rs 10.80 L
Cabinet and chargers: Rs 3.50 L
Install, electrical and civil: Rs 1.50 L
Capex per station: Rs 15.80 L
Monthly: electricity Rs 0.67 L, pump share Rs 0.20 L, battery depreciation Rs 0.18 L, software and service Rs 0.15 L
PRICE
Fixed monthly subscription with unlimited swaps. Rs 6,000 a month for two wheelers. Rs 6,000 introductory for autos, moving to Rs 7,500 at scale since an auto draws double the energy.
Contribution: Rs 1.50 L a month per station, payback in 18 to 24 months [7]
LAUNCH INVESTMENT
Rs 1.58 Cr for 10 stations, Rs 30 L software platform, Rs 20 L marketing and rider acquisition
Producing, Advertising, Distribution
Produce and source: modules assembled and tested in house from Indian ACC cell suppliers, cabinets sourced locally, packs stored and conditioned at one central Mumbai depot
Distribute and deliver: host model at partner petrol pumps on 100 to 150 sq ft with a revenue share of Rs 20,000 a month, so no land is purchased and the network scales fast
Service: IoT health monitoring of every pack, faulty packs pulled to the depot and replaced on the spot
Brand and logo: ____________, a battery cell set inside a circular swap arrow
Advertise and sell: onboarding desks at Rapido and Instamart rider hubs, WhatsApp rider groups, referral bonus of one free week, signage at partner pumps, regional language reels, tie ups with EV dealers at the point of sale
Sales Projections
 | YR1 | YR2 | YR3
Stations | 10 | 40 | 120
Sales Units | 450 | 1,800 | 5,400
Per Unit Price | Rs 6,000 | Rs 6,000 | Rs 6,500
Per Unit Contribution | Rs 3,300 | Rs 3,400 | Rs 3,600
Revenue | Rs 3.2 Cr | Rs 13.0 Cr | Rs 42.1 Cr

## Slide 3
Customer Evidence and Value Proposition
Based on seven face to face interviews with Rapido riders, Instamart delivery partners and CNG auto drivers in Mumbai
Team "____________" | EV Battery Swapping Network | ENT609 2025AUT
7 interviews
3 segments: bike taxi, delivery, CNG auto
5 of 7
ready to switch at Rs 6,000 per month
Rs 6,000
price point confirmed by four riders
1
Customer and Market Profile
Bike taxi riders, quick commerce delivery partners and CNG auto drivers, age 20 to 40
Daily running 80 to 150 km, monthly earning Rs 18,000 to 35,000
Reached through platform rider hubs and WhatsApp groups
India crossed 3,000 swap stations and USD 325 million investment by mid 2026 [1]
Mumbai serviceable base of commercial 2W and 3W fleets
2
Customer Unmet Need
Charging downtime directly cuts earning hours during the shift
Nearest swap station was up to 10 km away, so riders lost trips (Customer 1)
Rental EV at Rs 7,000 to 9,000 per month is unaffordable, so riders returned to petrol (Customer 4)
Riders want to own the vehicle and build an asset, not stay on rent
Fuel price hikes fall entirely on the driver
3
Current Option and Cost
Petrol bike: Rs 210 to 395 per day of fuel
CNG auto: Rs 325 to 390 per day plus 20 to 45 minutes in the refuel queue
Rental EV with unlimited swapping: Rs 7,000 to 9,000 per month, vehicle not owned
Pay per swap networks charge Rs 120 to 250 a swap [2]
Home charging: 4 to 6 hours, not possible mid shift
Value Proposition
For delivery riders, bike taxi riders and auto drivers in Mumbai who run 80 to 150 km every day
Who lose earning hours to charging and cannot afford a rental EV at Rs 7,000 to 9,000 a month
We ____________ operate a city wide battery swapping network hosted at partner petrol pumps
Offer unlimited two to three minute swaps on the rider's own electric vehicle, with no rental and no battery ownership
Which is faster than every charging option and fixed in price, unlike petrol and CNG which keep rising
At Rs 6,000 per month, unlimited swaps

## Slide 4
Why Electric Wins Over Petrol and CNG
Monthly running cost for a commercial user covering 2,800 km a month, at Mumbai prices of September 2026
Team "____________" | EV Battery Swapping Network | ENT609 2025AUT
Chart: Monthly running cost at 2,800 km
| Petrol bike | CNG auto | Rental EV | Our plan
Rupees per month | 6916 | 9126 | 8500 | 6000
Rs 2.47
petrol, per km
Rs 3.26
CNG auto, per km
Rs 0.44
electric, per km
4
Three Reasons the Shift Makes Sense Now
Fuel is expensive and still climbing. Petrol in Mumbai is Rs 111.18 per litre [3]. MGL raised CNG by Rs 2 to Rs 88 per kg from 1 September 2026, and the rate has moved from Rs 80 to Rs 88 within a year [4].
Energy cost falls by about 80 percent. An electric two wheeler uses roughly 40 Wh per km, which is Rs 0.44 per km at commercial tariff against Rs 2.47 per km on petrol.
Downtime disappears. A swap takes two to three minutes against 20 to 45 minutes in a CNG queue and 4 to 6 hours of home charging [2].
A fixed monthly price moves fuel price risk from the driver to us, which is the point our CNG auto customers responded to most strongly.
What This Means for the Rider
A CNG auto driver saves about Rs 3,100 a month and a petrol rider saves about Rs 900 a month, before counting the lower maintenance of an electric drivetrain. The subscription becomes clearly cheaper than pay per swap once the rider crosses roughly 140 km a day, which is why heavy commercial users are the right first customer.

## Slide 5
Technical Design of the Swap Network
One standard battery module serves both two wheelers and three wheelers, which keeps station inventory simple
Team "____________" | EV Battery Swapping Network | ENT609 2025AUT
1
Vehicle Coverage
L2 two wheeler, delivery and bike taxi: 2 modules, 4.0 kWh, about 100 km
L5M electric auto, passenger: 4 modules, 8.0 kWh
L5N electric auto, cargo: 4 modules, 8.0 kWh
L3 e-rickshaw: 2 modules, optional second phase
Not covered: cars, which need a robotic station costing crores
2
Battery Module
2.0 kWh, 48 V, LFP chemistry
10 to 12 kg so a rider can lift it by hand
Smart BMS with IoT tracking of charge cycles, temperature and state of health
AIS 156 compliant for thermal safety
Benchmark: industry swap packs run 1.5 to 2.5 kWh at 8 to 12 kg [2]
Honda Activa e: uses two 1.5 kWh packs; Piaggio Ape E-Xtra uses four 1.915 kWh modules [5]
3
Station and Charger
20 slot cabinet, 1 kW charger per slot at 0.5C
Module charges empty to full in about 2 hours
Connected load 20 kW, served by a 25 kVA LT commercial connection
No transformer or high power DC charger needed, unlike fast charging
Rider swap time 2 to 3 minutes
Footprint 100 to 150 sq ft at a partner petrol pump
4
The Interoperability Problem and Our Answer
The problem. India has no binding interoperability mandate for swappable batteries yet. Every network today runs a proprietary pack, so a Battery Smart pack will not power a Honda Activa e: [2][6]. Ola, Ather, Bajaj and TVS do not offer network swapping on their consumer scooters at all [2]. This means most personally owned electric two wheelers cannot use any swap network as they are sold.
Our answer. We standardise on a single 2 kWh module used in multiples, exactly as Piaggio and Sun Mobility already do across two and three wheelers [5]. We sign supply tie ups with fleet oriented OEMs whose vehicles accept this module, and we offer a retrofit bracket and connector kit for existing fleet EVs. Riders therefore keep owning their vehicle while we own and maintain every battery.

## Slide 6
Business Model, Go To Market and Projections
Unit economics of one 20 slot station serving about 45 subscribers, and the three year rollout plan
Team "____________" | EV Battery Swapping Network | ENT609 2025AUT
1
Unit Cost and Price
Item | Amount
40 packs at Rs 27,000 | Rs 10.80 L
Cabinet and chargers | Rs 3.50 L
Install, electrical, civil | Rs 1.50 L
Capex per station | Rs 15.80 L
Revenue, 45 subscribers | Rs 2.70 L / mo
Electricity, 180 kWh/day | Rs 0.67 L / mo
Pump partner share | Rs 0.20 L / mo
Battery depreciation | Rs 0.18 L / mo
Software and service | Rs 0.15 L / mo
Contribution | Rs 1.50 L / mo
Payback | 18 to 24 months
Price architecture: unlimited monthly subscription. Rs 6,000 for 2W, Rs 6,000 introductory for autos moving to Rs 7,500 at scale [7].
2
Go To Market
Produce: modules assembled and tested in house from Indian ACC cell suppliers, cabinets sourced locally
Distribute: host model at partner petrol pumps on 100 to 150 sq ft, revenue share of Rs 20,000 a month, no land purchase
Service: IoT health monitoring of every pack, faulty packs pulled to a central depot, riders never wait for repair
Sell: onboarding desks at Rapido and Instamart rider hubs, WhatsApp rider groups, referral bonus of one free week
Advertise: signage at partner pumps, regional language reels, tie up with EV dealers at point of sale
Launch investment: Rs 1.58 Cr for 10 stations, Rs 30 L platform, Rs 20 L marketing
3
Sales Projections
 | YR1 | YR2 | YR3
Stations | 10 | 40 | 120
Sales units | 450 | 1,800 | 5,400
Price / unit / mo | 6,000 | 6,000 | 6,500
Contribution / unit | 3,300 | 3,400 | 3,600
Revenue | 3.2 Cr | 13.0 Cr | 42.1 Cr
Key Risks We Have Priced In
Interoperability standard still not mandated by BIS [2]
Sun Mobility and IndianOil plan over 10,000 swap stations by 2030 on fuel retail sites [2]
Standalone batteries carry 18 percent GST against 5 percent on complete EVs [6]
References
[1] Mordor Intelligence, India Battery Swapping for Electric Two Wheelers Market, 2026. mordorintelligence.com/industry-reports/india-battery-swapping-for-electric-two-wheelers-market
[2] MeraEV, Battery Swapping in India 2026: Networks, Cost, Guide. meraev.com/blog/battery-swapping-electric-scooters-india-2026-guide
[3] Goodreturns, Petrol Price in Mumbai, September 2026. goodreturns.in/petrol-price-in-mumbai.html
[4] Equentis, CNG and PNG Price Hike, New Rates in Mumbai and Delhi NCR, September 2026. equentis.com/blog/cng-png-price-hike-new-rates-in-mumbai-and-delhi-ncr
[5] Piaggio Vehicles, Ape Electric Cargo Swappable Battery, technical specification. piaggio-cv.co.in/electric/electric-cargo-swappable-battery
[6] EVSelect, EV Battery Swapping in India 2026, How It Works, Networks and Costs. evselect.in/blog/ev-battery-swapping-india
[7] EVXpertz, Battery Swapping Business Models in India, 2W and 3W Swap Network Guide. evxpertz.com/blogs/battery-swapping-business-model-india
[8] IBEF, Emergence of Battery Swapping Stations and Battery Swapping EVs in India. ibef.org/research/case-study/emergence-of-battery-swapping-stations-and-battery-swapping-electric-vehicles-in-india